## Slide 1: DIO (LS-2-2101)
Static Configuration
  Rack #
  Slot #
  Banks 0-3
    Logic Threshold (%)
    Lines (Nx8)+1 -> (Nx8)+8, N = Bank #
      Line: Input = 1 or Output = 0
Dynamic Configuration
  None
MCP23S17 Addresses
  Bank 0 = 0b00
  Bank 1 = 0b01
  Bank 2 = 0b10
  Bank 3 = 0b11
MCP23S17 Digital Pin Configuration
MSB
LSB
Threshold Byte
Line (Nx8)+8
Line (Nx8)+1
…
Threshold Byte = [255 x Logic Threshold (%)]/100
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update Input/Output & Logic Config Reg = x12

## Slide 2: DIO in VeriStand

## Slide 3: FIU (LS-2-2611/LS-2-2610)
Static Configuration
  Rack #
  Slot #
  Banks 0-1
    Faults (Nx4)+1 -> (Nx4)+4, N = Bank #
      Initial Fault States: No Fault Output 1 = 0, Open Circuit 100 Hz = 1, Ground 100 Hz = 2, Open Circuit = 3, Ground = 4, Fail Rail 1 = 5, Fail Rail 2= 6, No Fault Output 2 = 7
Dynamic Configuration
  Fault States of Faults (Nx4)+1 -> (Nx4)+4
MCP23S17 Addresses
  Bank 0 = 0b00
  Bank 1 = 0b01
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update Fault States
Reg = x12
MCP23S17 Digital Pin Configuration
0
0
0
0
MSB
LSB
Fault (Nx4)+1
Fault (Nx4)+2
Fault (Nx4)+3
Fault (Nx4)+4

## Slide 4: FIU in VeriStand

## Slide 5: Battery Switch (LS-2-3010)
Static Configuration
  Rack #
  Slot #
  Banks 0
    Switch 1-3
      Switch: 1 = Battery Power to output, 0 = No battery power to output
Dynamic Configuration
  Switch channels 1-3 to battery power (=1) or no battery power (=0)
MCP23S17 Addresses
  Bank 0 = 0b00
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update
Reg = x12
MCP23S17 Digital Pin Configuration
MSB
LSB
Switch 1
Switch 2
Switch 3

## Slide 6: Battery Switch in VeriStand

## Slide 7: Wheel Speed Sensor (LS-2-2751)
Static Configuration
  Rack #
  Slot #
  Bank 0
    Channels 1-4
      Channel: Current Mode = 1, Voltage Mode = 0
Dynamic Configuration
  Change mode channel by channel
MCP23S17 Addresses
  Bank = 0b00
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update
Reg = x12
MCP23S17 Digital Pin Configuration
MSB
LSB
Channel 1
Channel 2
Channel 3
Channel 4

## Slide 8: Wheel Speed Sensor in VeriStand

## Slide 9: Resistor Board (LS-2-2901)
Static Configuration
  Rack #
  Slot #
  Banks 0-7 = Channels 0-7
    Resistance = 2 Ohm + (Bit 0) *2^-3 + (Bit 1)*2^-2 + … + (Bit 15)*2^12
Dynamic Configuration
  Change resistance
MCP23S17 Addresses
  Bank 0 = 0b0000
  Bank 1 = 0b0001
  Bank 2 = 0b0010
  Bank 3 = 0b0011
  Bank 4 = 0b0100
  Bank 5 = 0b0101
  Bank 6 = 0b0110
  Bank 7 = 0b0111
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update
Reg = x12
MCP23S17 Digital Pin Configuration
MSB
LSB
Channel N
Channel N

## Slide 10: Resistor in VeriStand

## Slide 11: UEGO (LS-2-2801)
Static Configuration
  Rack #
  Slot #
  Hardware Settling Time (us)
  Calibration Time (us)
MCP23S17 Addresses
  None
Assert CS
Assert Calibration
Deassert Calibration
Deassert CS
CS
Cal
Calibration Time
Hardware Settling Time

## Slide 12: UEGO in VeriStand

## Slide 13: Current Sense (LS-2-2202)
Static Configuration
  Rack #
  Slot #
  Bank 0
    Line 1 -> Line 16
      Line: 1 = Calibration Active, 0 = Calibration Inactive
Dynamic Configuration
  Set Line X to calibrate (set pin = 1) where X = Line # (single VeriStand channel). Only one line can be calibrated at a time. If the channel < 1 or > 16, the system is not calibrating. If the channel >= 1 and <=16, the channel is being calibrated (Line # = Channel value). The user should look at the corresponding AI channel to get offset value.
MCP23S17 Addresses
  Bank 0 = 0b00
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update
Reg = x12
MCP23S17 Digital Pin Configuration
MSB
LSB
Line 1
Line 16
…

## Slide 14: LEDs on Backplane
Static Configuration
  Rack #
  Slot 0 only
  Banks 0
    LED 1 -> LED 8
      Line: 1 = ON, 0 = OFF
Dynamic Configuration
  LED 1 -> LED 8
    Line: 1 = ON, 0 = OFF
MCP23S17 Addresses
  Bank 0x00
Switch to Bank 0
Reg = x05
Data = x0000
Config for Sequential Addressing
Reg = 0x0A
Data = x08
Change Mode to Outputs
Reg = x00
Data = x0000
Update
Reg = x12
MCP23S17 Digital Pin Configuration
MSB
LSB
Line 1
Line 8
…