## Slide 1
CLCK Polarity =0
CLCK PHASE =0
Clock Line = low
Set MOSI Data bit
Set Clock Line =high
Chip Select
SPI Requirements.
The SPI Driver shall be compatible with the MCP23017 SPI chipset
The SPI shall control
  Setup for Digital (input or output, threshold, reference voltage tied to bank of 8)
  Fault Insertion
  Control Resistor on the UEGO board
SPI lines
  Clock
  Master In
  Master Out
  Chip Select (1 per Leucadia Card)
The pins shall be controlled as defined:
Pin 11 MOSI
Pin 12 CLOCK
Pin 13 MISO
Pin 1 CS7
Pin 2 CS6
Pin 3 CS5
Pin 4 CS4
Pin 5 CS3
Pin 6 CS2
Pin 7 CS1
Pin 8 CS0
The driver shall work for either the NI 9403 or NI 784xr series board
The Clock polarity shall be configurable
The Clock phase shall be configurable
The Clock speed shall be configurable
The Clock polarity is defined as 0
The Clock phase is defined as 0
The Clock speed is defined as 10 kHz

## Slide 2
Clock Speed 10 KHz
Chip select
Control Byte (Write)
01000(A1)(A0)0
Register Address
0x0C
Data 16 bit
(first 8 bits are threshold second 8 bits are direction)
Register Address
0x00
Data 16 bit of all 0
Control Byte
01000(A1)(A0)0
Digital I/O Board
Digital I/O SPI Requirements.
The MCP23017 SPI chipset shall use Bank =0
Four MCP23017 SPI chips are used on the board. Each SPI chip controls a Bank of 8 pins. The Addresses of the four banks are:
Addresses
Pin 1-8 A1=0 A0=0
Pin 9-16 A1=0 A0=1
Pin 17-24 A1=1 A0=0
Pin 25-32 A1=1 A0=1
The SPI expects a Control Byte followed by a Register Address and then Data if writing.
Register Address 0x00 is used to set the initial state of the SPI GPIO to outputs
Register Address 0x0C is used to set the value of the GPIO of the outputs
The first 8 bits sets the threshold for this bank. The threshold is Ref x N/256, where N is the 8 bit binary number. Positive Logic, ON=1. LSB is pin 1
The second 8 bits set the output mode. Each bit controls the state of one channel. By default the channels are set to inputs.
Register Address
0x0C
Control Byte
(read)
01000(A1)(A0)1
Read Data and Verify Command

## Slide 3
Clock Speed 10 KHz
Chip select
Control Byte
Set Threshold
010000(A0)0
Register Address
0C
Data 16 bit
Register Address
00
Data 16 bit of all 0
Control Byte
Set Threshold
010000(A0)0
Register Address
0x0C
Control Byte
(read)
01000(A1)(A0)1
Read Data and Verify Command
FIU I/O SPI Requirements.
The MCP23017 SPI chipset shall use Bank =0
Two MCP23017 SPI chips are used on the board. Each SPI chip controls a Bank of 8 pins. The Addresses of the Two banks are:
Addresses
Pin 1-4 A0=0
Pin 5-8 A0=1
The SPI expects a Control Byte followed by a Register Address and then Data if writing.
Register Address 0x00 is used to set the initial state of the SPI GPIO to outputs
Register Address 0x0C is used to set the value of the GPIO of the outputs
Three bits sets the Failure for each channel. Bits 3, 7, 11, 15 are not used and should be set to 0. Bits 0,1,2 correspond to C,B,A in the Control Truth Table for Failure Channel 1 or 5 (depending on the address A0). Likewise Bits 4,5,6 correspond to C,B,A in the Control Truth Table for Failure Channel 2 or 6 (depending on the address A0).